## Slide 1
Introduction to the
Decentralised Treatment Facility (DTF)
UBSUP

## Slide 2
Low Income Area
Pit latrines
Septic tanks
UDDT
Sanigo
Exhauster
Exhauster
DTF
THE CONCEPT

## Slide 3
1
2
3
4
5
6
7
Receiving Bay / Balancing tank (RBBT)
Settler (ST)
Anaerobic Baffled Reactor (ABR)
Vertical Flow Constructed Wetland (VFCW)
Sludge Drying Reed Beds (SDRB)
Composting Area (CA)
Operator Store (OS)
THE DTF MODULES

## Slide 4
THE TREATMENT
 Mechanical and biological treatment
NO CHEMICALS !!
NO ELECTRICITY !!
 DTF runs by gravity

## Slide 5
IN DETAILS
1
Operator Store
Operator’s office
Entrance registration desk
Storage room for equipment
2
Receiving Bay / Balancing Tank
Screening of the coarse material
Storage of the effluent
Flow control to provide constant inflow to the DTF

## Slide 6
IN DETAILS
3
Settler
2 consecutive chambers separated with a baffle wall
Sedimentation of settable solid
Flotation of fat and oil
4
Anaerobic Baffled Reactor
2 rows of 6 consecutive chambers with down pipes  anaerobic treatment through the settled sludge
1 siphon chamber  to release intermittent flow

## Slide 7
IN DETAILS
5
6
7
2 basins filled with successive gravel and sand layers planted with aquatic plants
Perforated pipes on top (to feed) and at the bottom (to receive)
FiItration, and aerobic treatment
Vertical Flow Constructed Wetland
Sludge Drying Beds
2 to 4 non planted beds filled with successive gravel and sand layers
Filtration and evaporation
Composting Area
Composting shed
Mix dry sludge and organic waste to produce compost