## Slide 1: «Water Sector Reform in Kenya »
Trainings 24.-28.8. and 28.9.-2.10.2015

## Slide 2: Introduction to Wastewater
Based in parts on DWA/Engicon „Introduction to Wastewater“, modified by Margraf Publishers

## Slide 3
Table of Content
  What is wastewater
  Types of wastewater
  Wastewater collection
  Wastewater quality
  Wastewater: importance and reasons for treatment

## Slide 4
  What is wastewater?
  All types of wastewater emitted from various human activities (domestic, commercial, industrial)
  sometimes called sewage or wastewater because they are often transported in the public sewage network

## Slide 5
Water turns to wastewater

## Slide 6
  Types of wastewater (I)
  There are two types of wastewater:
  1- Domestic wastewater
  The water resulting from human use in homes, bathrooms, kitchens, laundries and toilets, which may include industrial liquid waste discharges are allowed to sewage networks linking the public in accordance with instructions issued by the official authorities and receive home filtration plants operating in the country

## Slide 7: Domestic wastewater: What products are we dealing with?
Greywater: wastewater from kitchen, bath, shower.
Yellow-water:
separated urine
Blackwater: urine, faeces & flush
Faecal sludge: solids and liquids accumulating in sanitation systems
A sanitation system must manage all products generated !
Excreta: urine & faeces
Introduction
Notes: Key messages
Households produce different waste products.
A sanitation system must deal with all products generated.
Next slide: What are the characteristics of waste products?
Additional information & questions:
The generation of liquid waste from human activities is unavoidable. However, not all humans produce the same amount of liquid waste. The type and amount of liquid waste produced in households is influenced by behaviour, lifestyle and standard of living of the population as well as by the governing technical and juridical framework. (Henze and Ledin 2001, pp. 57-72)
The following section describes the different liquid waste fractions produced by the households. Industrial wastewater is not included, although it makes up an important fraction of wastewater in some environments. (Tilley 2007, pp. 2)
Blackwater is the mixture of urine, faeces and flushing water, along with anal cleansing water (if anal cleansing is practiced) or dry cleansing material (e.g. toilet paper).
Greywater is used water which results from bathing, hand-washing, cooking or clothes-washing. It is sometimes mixed with, or treated along with, other types of products
Urine is urine that is not mixed with any faeces or water.
Faeces refers to (semi) solid excrement without any urine or water.
Excreta is the mixture of urine and faeces that is not mixed with any flushing water (although small amounts of anal cleansing water may be included).
Faecal Sludge is the general term for the undigested, or partially digested slurry or solid that results from the storage or treatment of blackwater or excreta.
Why distinguish between so many products?

## Slide 8
  Types of wastewater
  2- Industrial wastewater
  The water resulting from the activity and industrial production are divided into two parts:
  Industrial Wastewater connected to the sewage system and delivered to the wastewater treatment plants as wastewater mixed household wastewater.
  Industrial wastewater not connected to the network and that is put into the environment in different ways such as rivers, streams and ocean or exploited for agricultural purposes.

## Slide 9
  Wastewater collection networks
  Sewerage network
  The networks that collect household wastewater, industrial and commercial
  Storm water network
  The networks that discharge storm water and street wash water only
  Combined system
  The networks that conduct various types of water regardless of its source, household, industrial or rain water

## Slide 10
  What do we mean by quality?
  When we talk about the quality of water, whether drinking water or wastewater,
  we're talking about the properties of this water and
  the extent of being complying with the national and international standards of the drinking water and wastewater quality.

## Slide 11
  The importance of wastewater (reuse)
  Due to the scarcity of water resources,
  increasing population, rising standard of living and
  increased demand for agricultural and industrial water and economic development, trade and tourism,
  the waste water is regarded as an important and strategic part of the water budget in many countries
  where it is considered as an important source of water to be exploited in various areas.

## Slide 12
  Reasons for wastewater treatment
  Protection of surface water and groundwater and the environment from pollution in general
  Prevention of the spread of diseases and epidemics
  Avoidance of the inconvenience and harassment of people
  Re-use of water after treatment for various agricultural and industrial purposes