## Slide 1: Upscaling Basic Sanitation for the Urban Poor (UBSUP)
DTF Site Selection Site Surveying

## Slide 2
Objective: You are able to collect data required to prepare the final design

## Slide 3: Content
Questions you might to ask yourself:
What is the context of this session?
How is this tool used?
May I try it with my colleagues?

## Slide 4: What is the context of this session?
all info can be found in your manual
The UBSUP SafiSan Toolkit

## Slide 5: How is this tool used?
The tool consists of 3 parts:
A template layout plan to capture required information
Templates of tables to note required data
A step-by-step instruction which data to be collected, and how

## Slide 6: Step 1 – Boundaries of DTF site
Mark corners (e.g. with metal rods)
Take preferably GPS coordinates of cornerstones
Note distances on the layout drawing
Ensure sufficient distance (riparian) to water bodies as per NEMA

## Slide 7: Step 2 – Raster levelling
Define a fix and suitable benchmark (should also be used during construction, visible from the entire site to avoid transfers)
Mark location of BM on layout drawing and permanently at site
Take levels according to a fix raster with 20-30 points
Note levels with a clear reference to the location at provided template
„Levelling“ is explained in the next session
Reference Point | Level (m)
B.M. | 0.000
A1 | 
A2 | 
A3 | 
... | 
... | 

## Slide 8: Step 3 – Arrangement of modules
Draw modules: e.g. treatment of FS and UDDT matter on a new layout plan
Consider space for manoeuvring of exhauster trucks
Ensure proper arrangement of pipes and inspection boxes
Don´t forget proper arrangement of bypass pipes

## Slide 9: Step 4 – Levelling at particular locations
Take levels at the following locations
  Level of the final effluent discharge point (flooding level)
  Ground levels where different treatment modules will be located
  Existing ground level where the RB will be located
  Existing ground level at gate
Note levels in table template with clear reference
Reference Point | Level (m)
B.M. | 0.000
Outlet | 
VFCW | 
CA | 
ABR | 
... | 
Required to check whether pumping required

## Slide 10: Step 5 – Measurement of distances
Take distances between the treatment modules that are arranged in series:
  VFCW outlet to final discharge point
  Outlet of ABR-BT to VFCW
  ST outlet to ABR inlet
  Outlet of RB/BT to ST inlet
Note distances on layout plan and in table
Pipe slopes will lead to required levels of modules
Reference | Distance (m)
A | 
B | 
C | 
D | 

## Slide 11: Step 6 – Determination of soil conditions
Establish soil conditions at all locations where excavation is required
  Particularly for ST and ABR (underground)
  But also all modules (foundation)
Note levels in table template with clear reference
Reference Point | Soil conditions
RB/BT | 
ST | 
ABR | 
VFCW | 
SDRB | 
CA | 
House | 
Soil conditions determine excavation cost in BoQ

## Slide 12: May I try it with my colleagues?
Field Trip & Group Exercise “Site Surveying”:
Please arrange required modules (RB/BT, ST, ABR, VFCW, SDRB, CA) on a title block within your DTF technical teams
Discuss with other participants and trainers the layout
Measure required dimensions and levels and fill into provided tables
We will have a field trip to a potential site where you can apply the tool
For this purpose you will get 5 empty title blocks and several table templates to be filled
Prior to that, you will learn how a levelling machine is used

## Slide 13: Do you have any questions, remarks or suggestions?