## Slide 1: Upscaling Basic Sanitation for the Urban Poor (UBSUP)
Background information needed for the Levelling
for a DTF

## Slide 2: Levelling
In this session you learn:
What is a benchmark and how to set it up?
Which levels are determining the future set up of the DTF?
What are the important levels for a DTF?
How to read the cross-sectional drawings?
How to level with the collimation method?
Group work

## Slide 3: What is a benchmark?
A benchmark is a fixed reference point which does not change during the entire project time
Usually defined at 100,000m altitude
Should be visible from all points of the construction side
All existing and future level points have to be calculated in reference to this reference point

## Slide 4: How to set up a benchmark?
Choose a fixed point at an existing and permanent structure (e.g. electricity poste, existing building) or fix your own benchmark at the construction side.
Electricity pole with a nail
Concreted marker stone

## Slide 5: What are the important levels for a DTF?
We have to calculate backwards from the effluent discharge point
1
ST
VFCW
RBBT
ABR
1%
1%
1%
3
2
4
1%

## Slide 6: How to read the cross-sectional drawings?
Cross sectional drawings are provided in the next training for Design adaptation
Level differences have to be defined individually by the DTF technical team depending on the positioning of the modules

## Slide 7: How to use the optical level?
Introduction to the instrument
Level the instrument by adjusting the levelling screws.
The bubble to be central in the circle.
Turn the telescope through 180º
Parallax is the apparent movement of the cross-hairs over the levelling staff when the eye is moved up and down while sighting through the instrument.

## Slide 8: How to use the optical level?
Introduction to the instrument
Sight onto the levelling staff.
Focus the telescope on the staff.
Always ensure the bubble is central
Take the reading of height.
Each square is 1cm (10mm)
First metre is black and second metre is red
Each E is 100mm (0.1m) apart

## Slide 9: How to level with the collimation method
BM
The temporary benchmark and height of collimation
BM: Benchmark = 100,000
Decide for an BM

## Slide 10: How to level with the collimation method
No1= BM
The temporary benchmark and height of collimation
BM: Benchmark = 100,000
HoC
=X
HoC: Height of Collimation = OBM + X
“Place the rod on top of the BM”
The booking of the levels is done at the same time the reading is taken

## Slide 11: How to level with the collimation method
Rules of booking or “the surveyor language”
BS
IS
IS
BS
IS
FS
FS
BS= Back Sight =
the first reading from a new instrument position
IS= Intermediate Sight= occurs between the Back Sight and Foresight
FS= Foresight=
is always the last reading from an instrument position
After moving the optical level the booking procedure remains the same

## Slide 12: How to level with the collimation method
BS
IS
IS
FS
1,056
No.1:
BM=100,000
HoC1=
100,000+1,056
Rules of booking or “the surveyor language”
HOC1=101,056 to be added in diagram
BM is the first reduced level!

## Slide 13: How to level with the collimation method
No. | Backsight (BS) | Intermediate Sight (SI) | Fore Sight (FS) | Height of Collimation | Reduced level (RL) | Remarks
1 | 1,056 |  |  | 101,056 | 100,000 | Benchmark
Rules of booking or “the surveyor language”
Fill in first reading
= height of optical level
Number it!
Name the reading
First reduced level!

## Slide 14: How to level with the collimation method
BS
Rules of booking or “the surveyor language”
IS
IS
FS
No.4=
101,056-1,575=
99,481
No.2=
101,056-2,017=
99,039
No.3=
101,056-2,398=
98,658
1,056
No.1= BM=100,000
2,017
2,398
1,575
HoC1=
100,000+1,056

## Slide 15: How to level with the collimation method
Diagram for booking readings
No. | Backsight (BS) | Intermediate Sight (SI) | Fore Sight (FS) | Height of Collimation | Reduced level (RL) | Remarks
1 | 1,056 |  |  | 101,056 | 100,000 | Benchmark
2 |  | 2,017 |  |  | 99,039 | 
3 |  | 2,398 |  |  | 99,658 | 
4 |  |  | 1,575 |  | 99,481 | Change Point
Fill readings into the diagram
minus
Leads to the reduced levels

## Slide 16: How to level with the collimation method
BS
Rules of booking or “the surveyor language”
IS
IS
BS
IS
FS
FS
No.4=
101,056-1,575=
99,481
No.2=
101,056-2,017=
99,039
No.3=
101,056-2,398=
98,658
No.5=
101,657-1,839=
99,818
No.6
DP=
101,657-2,539=
99,118
No.1=
BM=100,000
HoC1=
100,000+1,056
2,176
1,839
2,539
HoC2=
HoC1-1,575+2,176=101,657
1,056
2,017
2,398
1,575
Rod must remain in the old position until the first reading from the new position has been completed!

## Slide 17: How to level with the collimation method
Diagram for booking readings
No. | Backsight (BS) | Intermediate Sight (SI) | Fore Sight (FS) | Height of Collimation | Reduced level (RL) | Remarks
1 | 1,056 |  |  | 101,056 | 100,000 | Benchmark
2 |  | 2,017 |  |  | 99,039 | 
3 |  | 2,398 |  |  | 99,658 | 
4 | 2,176 |  | 1,575 | 101,657 | 99,481 | Change Point
5 |  | 1,839 |  |  | 99,818 | 
6 |  |  | 2,539 |  | 99,118 | Discharge point
Fill in the new readings
Calculate the Height of collimation for the new position:
HoC2=
101,056-1,575+2,176= 101,657
Reduced level (RL) for Discharge point= 101,657-2,539=99,118

## Slide 18: How to level with the collimation method
Diagram for booking readings
No. | Backsight (BS) | Intermediate Sight (SI) | Fore Sight (FS) | Height of Collimation | Reduced level (RL) | Remarks
1 | 1,056 |  |  | 101,056 | 100,000 | Benchmark
2 |  | 2,017 |  |  | 99,039 | ST
3 |  | 2,398 |  |  | 99,658 | ABR
4 | 2,176 |  | 1.575 | 101,657 | 99,481 | Change Point
5 |  | 1,839 |  |  | 99,818 | VFCW
6 |  |  | 2,539 |  | 99,118 | Discharge point
 | 3,232 |  | 4,114 |  |  | 
Calculation double check:
∑F.S - ∑B.S = first reduced level – last reduced level
Example:
4,114-3,232=100,000-99,118
0,882 = 0,882
∑
∑

## Slide 19: How to level with the collimation method
BS
Calculate the reduced level at the Discharge point (DP)
IS
IS
BS
IS
FS
FS
Transfer point=?
ST outlet=?
ABR outlet=?
VFCW outlet=?
DP=?
BM=1,800.00m
HoC1= BM+BS=?
2.67m
2.78m
3.02m
0.52m
2.45m
2.56m
2.27m
HoC2=
HoC1-FS+BS=?

## Slide 20: How to level with the collimation method
No. | Backsight (BS) | Intermediate Sight (SI) | Fore Sight (FS) | Height of Collimation | Reduced level (RL) | Remarks
1 | 0.52m |  |  | 1,800.52m | 1,800.00m | Benchmark
2 |  | 2.45m |  |  | 1,799.48m | ST= 1,800.00-2.45
3 |  | 2.56m |  |  | 1,797.44m | ABR= 1,800.00-2.56
4 | 2.67m |  | 2.27m | 1,800.92m | 1,798.14m | Change Point
5 |  | 2.78m |  |  | 1,798.14m | VFCW
6 |  |  | 3.02m |  | 1,797.90m | Discharge point
 | 3.19m |  | 5.29m |  |  | 
Calculation double check:
∑F.S - ∑B.S = first reduced level – last reduced level
Example:
5.29m-3.19m=1,800.00m-1,797.90m
2.1m=2.1m
∑
∑
Calculate the reduced level at the Discharge point (DP)
Double Check the calculation!

## Slide 21
Group Exercise within the DTF technical team :
Time: 20min
Type of exercise: group work of technical DTF team
Transfer the example readings for BS, IS, FS into the booking diagram
Calculate the reduced levels for OBM, Settler outlet, ABR, Temporary Benchmark, VFCW and Discharge Point
Do a calculation double check

## Slide 22: How to level with the collimation method
Diagram for booking readings
No. | Backsight (BS) | Intermediate Sight (SI) | Fore Sight (FS) | Height of Collimation | Reduced level (RL) | Remarks
1 | 1.83 |  |  | 1,801.83 | 1,800.00 | BM
2 |  | 0.89 |  |  | 1,800.94 | RB outlet
3 |  | 2.49 |  |  | 1,799.34 | ST outlet
4 | 2.06 |  | 3.27 | 1,800.62 | 1,798.57 | ABR outlet / Ch- point
5 |  |  | 3.66 |  | 1,796.96 | DP
 | ∑BS: |  | ∑FS: |  |  | 

## Slide 23: Do you have any questions, remarks or suggestions?