## Slide 1: Upscaling Basic Sanitation for the Urban Poor (UBSUP)
Preparation of final design Technical Drawings Plan View

## Slide 2: Content
Questions you might to ask yourself:
What is the context of this session?
How do potential DTF layouts looks like?
What has to be considered during layout preparation?

## Slide 3: What is the context of this session?
The SafiSan Toolkit
This session

## Slide 4: How do potential DTF layouts looks like?
VFCW
VFCW
SDRB
ABR
ST
RB/BT
Storage
CA

## Slide 5: How do potential DTF layouts looks like?
VFCW
VFCW
SDRB
ABR
ST
RB/BT
Storage
CA

## Slide 6: How do potential DTF layouts looks like?
VFCW
VFCW
SDRB
ABR
ST
RB/BT
Storage
CA

## Slide 7: How do potential DTF layouts looks like?
VFCW
VFCW
SDRB
ABR
ST
RB/BT
Storage
CA

## Slide 8: Baseline data collection - Boundaries
Mark corners (e.g. with metal rods)
Ensure sufficient distance (riparian) to water bodies as per NEMA

## Slide 9: Design - Boundaries

## Slide 10: Baseline data collection - Raster levelling
Take levels according to a fix raster (20-30 points)
► To consider the existing ground level/ topography during the proper arrangement of the modules!

## Slide 11: Design – Raster Levelling

## Slide 12: Baseline data collection - Arrangement
Arrange all required modules in an operational manner
Consider space for manoeuvring of exhauster trucks
Consider access for exhauster trucks to ST and ABR for de-sludging
Consider access to all treatment modules for O&M
Ensure proper arrangement of pipes, bypass pipes and inspection boxes
► To determine in the BoQs the number of inspection/bypass chambers!

## Slide 13: Excursion: How are ST and ABR de-sludged?
To avoid a fixed pumping station (requires energy) exhauster trucks can be used to de-sludge the DTF modules
  Exhausters pump sludge from bottom of ST and ABR (pump head approx. 3m)
  Exhausters discharge sludge by gravity on top of SDRB (via hose)
  ► SDRB surface must be constructed slightly lower than discharge valve of exhauster truck
  ► SDRB outlet pipe must be constructed slightly higher than the inlet of the receiving treatment module (according to the DTF layout either the RB or ST or ABR or VFCW)
  ► To be considered in preparation of cross-section

## Slide 14: Design - Arrangement
VFCW
VFCW
SDRB
ABR
ST
RB/BT
Storage
CA
Operation
Regular Maintenance
Occasional Maintenance

## Slide 15: Baseline data collection - Distances
Determine distances:
  VFCW outlet to final discharge point
  Outlet of ABR-BT to VFCW
  ST outlet to ABR inlet
  Outlet of RB/BT to ST inlet
  Drainage pipe from SDRB to ABR/VFCW
  (Bypass pipes)
  (Site boundaries)
► Required to determine in the BoQs the length of PVC pipes (connection & bypass)!

## Slide 16: Design – Distances
VFCW
VFCW
SDRB
ABR
ST
RB/BT
Storage
CA
A
B
C
D
Examples:
A: 40m
B: 7m
C: 9m
D: 4m
E: 4m
E

## Slide 17: Do you have any questions, remarks or suggestions?